## Slide 1
THERMAL-AWARE
QUBIT MAPPING
OPTIMIZATION
Improving Quantum Circuit Reliability on NISQ Devices
Qiskit
NetworkX
Python
NISQ
Quantum Computing Project | Thermal-Aware Mapping

## Slide 2
THE PROBLEM
Why standard qubit mapping fails on real hardware
01
Sparse Connectivity
Qubits are not fully connected. Gates between non-adjacent qubits require SWAP decomposition — each costing 3 CX gates.
02
Thermal Heterogeneity
Qubit temperatures vary across the chip. Error rates differ by 2-5x. T1/T2 times range from 50μs to 300μs on the same device.
03
Thermally Blind Routing
SABRE and standard transpilers optimize only for SWAPs. They ignore which physical qubits are noisy, hot, or unstable.
💡 Result: Critical qubit operations may run on the noisiest, hottest, shortest-lived physical qubits

## Slide 3
THE CORE IDEA
Optimize SWAP cost AND thermal noise simultaneously
Minimize = α × SWAP_cost + β × Thermal_noise_cost
where α = 0.6 (connectivity weight) β = 0.4 (thermal weight)
Standard Mapping
✗ Connectivity only
✗ SWAP minimization only
✗ Thermally blind
✗ May use hot/noisy qubits
Thermal-Aware Mapping
✓ Connectivity + thermal noise
✓ SWAP + decoherence cost
✓ Stability-ranked assignment
✓ Coolest qubits selected first
→

## Slide 4
HARDWARE & THERMAL MODEL
Device topology as a graph + per-qubit noise profiles from calibration data
Hardware Topology — 6 Edges, 5 Qubits
q0
12K
q1
18K
q2
10K
q3
20K
q4
15K
Direct connection
Cross link
Test Circuit — 5 CX Gates
q0
q1
q2
q3
q4
+
+
+
+
+
CX
0,4
CX
1,3
CX
0,3
CX
2,4
CX
1,4
Hardware Topology (NetworkX Graph) | Edges: (0,1)(1,2)(2,3)(3,4)(0,2)(1,3)
Qubit
Temp (K)
Error Rate
T1 (μs)
T2 (μs)
Stability
q2
10
0.001
150
110
0.97 ★
q0
12
0.002
120
80
0.92
q4
15
0.0025
110
75
0.88
q1
18
0.003
95
60
0.85
q3
20
0.004
80
50
0.78 ✗

## Slide 5
THREE MAPPING STRATEGIES
Adversarial baseline → Industry standard → Thermal-aware innovation
01
Random Mapping
Adversarial Baseline
Deliberately assigns logical qubits to maximally distant physical qubits. Reversed layout maximizes routing distance on the linear topology.
7 SWAPs
0.951
SWAPs
Fidelity
02
SABRE Mapping
Industry Standard
Swap-based Bidirectional heuristic search. Near-optimal routing but zero thermal awareness. May use hot/unstable qubits.
1 SWAP
0.968
SWAPs
Fidelity
03
Thermal-Aware
My Innovation
Assigns coolest, most stable qubits first. Uses SABRE for routing after thermally optimal initial layout assignment.
2 SWAPs
0.974
SWAPs
Fidelity

## Slide 6
SYSTEM ARCHITECTURE
6-module pipeline from circuit input to optimized output
circuit_loader.py
Generates Bell, GHZ, QFT, Random circuits
→
topology_model.py
NetworkX hardware graph, connectivity
→
thermal_model.py
CSV noise data → Qiskit NoiseModel
mapping_algorithm.py
ThermalAwareMapper + RandomMapper
→
optimizer.py
Runs transpile() for all 3 methods
→
evaluator.py
Fidelity via ideal vs noisy simulation
↓ ↓ ↓
main.py → Terminal Report + 4 PNG Plots saved to results/graphs/

## Slide 7
RESULTS & ANALYSIS
Thermal-aware mapping achieves highest fidelity despite modest SWAP overhead
Method
SWAP Count
Noise Score
Fidelity
Verdict
Random
7
0.51
0.951
Worst ✗
SABRE
1
0.51
0.968
Good
Thermal
2
0.51
0.974
Best ✓
SWAP Count
7
Random
1
SABRE
2
Thermal
Fidelity
0.951
Random
0.968
SABRE
0.974
Thermal
Key Insight: 1 extra SWAP over SABRE is offset by cooler qubit quality — Thermal wins on Fidelity

## Slide 8
ACTUAL OUTPUT — GENERATED GRAPHS
Real plots produced by running python main.py on the project
full_summary.png
SWAP Count · Noise Score · Fidelity
topology_graph.png
Random: 7 SWAPs
SABRE: 1 SWAP
Thermal: 2 SWAPs
Best Fidelity: Thermal (0.974)

## Slide 9
KEY TOOLS USED
Qiskit
Quantum Layer
QuantumCircuit, transpile(), CouplingMap, SabreSwap
Qiskit Aer
Simulator
AerSimulator, NoiseModel, thermal_relaxation_error
NetworkX
Graph Layer
Hardware topology, shortest paths, neighbor lookup
NumPy
Math Layer
Matrix operations, fidelity calculations, arrays
Pandas
Data Layer
Loads thermal_noise.csv, manages results table
Matplotlib + Seaborn
Visualization
4 PNG charts: SWAP, Noise, Fidelity, Summary

## Slide 10
REAL-WORLD IMPACT & FUTURE WORK
Real-World Relevance
→ Applies to IBM Quantum, Google Sycamore, IonQ
→ NISQ devices limited by coherence depth ~333 gate layers
→ Qubit error rates vary 2-5x across same chip
→ Current IBM transpiler ignores thermal profiles
→ This approach is a genuine research direction
Future Extensions
→ Dynamic thermal remapping mid-circuit
→ Live IBM calibration data via IBMRuntimeService
→ Pareto optimization of SWAP vs thermal cost
→ Crosstalk-aware noise modeling
→ RL agent for thermal-aware routing policy

## Slide 11
SUMMARY
A smarter qubit mapping algorithm that assigns quantum operations to the coolest, most stable physical qubits first — reducing thermal noise errors beyond what standard routing achieves.
01
Thermal noise is spatially heterogeneous on real NISQ devices
02
Standard transpilers are thermally blind — a real gap to fill
03
Thermal-aware mapping improves fidelity: 0.974 vs 0.968 (SABRE)
04
Groundwork for dynamic remapping and real hardware integration
Thermal-Aware Qubit Mapping Optimization | Quantum Computing Project